## Slide 1
GOES-R ABI Sounding Algorithm Development:
“ABI+PHS” Approach and Processing of Cloudy Observations
Stanislav Kireev1 and William L. Smith1,2
1Center for Atmospheric Sciences, Hampton University, VA
2University of Wisconsin - Madison, WI
8th NOAA-CREST Annual Symposium, New York, 5-6 June, 2013

## Slide 2
HU participates in NOAA GOES-R preparation and risk reduction activities (GOES-R ABI Algorithm Working Group)
Two main focuses of the HU research:
Develop ABI+PHS approach to improve the accuracy of ABI retrievals;
Enhance retrieval algorithm with ability to process all-sky (clear and cloudy) observation conditions.

## Slide 3
ABI Full Disk Scan
Figure credit: ITT Industries
The primary instrument on GOES-R satellite
Broad-band visible & IR spectrometer
Imaging Earth’s weather
High spatial and temporal resolution
Scheduled for flight in 2015
Retrieve products include:
      Air temperature
      Water vapor
      Ozone
      Surface properties
      Cloud properties
      …
What is Advanced Baseline Imager (ABI):

## Slide 4
10 ABI IR Bands:
6 ABI Vis/Near-IR Bands:
Polar Hyperspectral Satellite (PHS)
1000s of spectral channels =>
  Higher actual retrieval SNR
  Higher vertical resolution
  Higher accuracy of retrieved products
But…
Lower spatial resolution (12-15 km footprint)
Lower temporal resolution (twice per day over the same area)

## Slide 5
The primary goal of ABI+PHS approach is to combine high spatial and temporal resolution of ABI observations with high vertically resolved and accurate retrievals that can be obtained with hyperspectral instrument.
The combination of both instruments is especially important for observations of rapidly developing hazardous weather conditions (severe storms, hurricanes, flooding, tornadoes, etc.)
Latest approaches to incorporate PHS soundings into ABI retrievals:
Temporal difference:
XABI+PHS(t1) = XPHS(t0) + XABI(t1) - XABI(t0)
Center retrieval around PHS state:
XABI+PHS(t1) - XPHS(t0) = G [RABI(t1) – RABI/PHS(t0)]

## Slide 6
Joint Airborne IASI Validation Experiment (JAIVEx):
the perfect Cal/Val campaign to test ABI+PHS
US-European collaboration focusing on the validation of radiance and geophysical products from MetOp-A
(1st advanced sounder in the Joint Polar Satellite System)
Location/dates
  Houston, TX, DOE ARM CART site, OK, Gulf of Mexico
  14 Apr–4 May, 2007
Aircrafts
  NASA WB-57 (NAST-I, NAST-M, S-HIS)
  UK BAe146-301 (ARIES, MARSS, Deimos, SWS; dropsondes)
Satellites
  MetOp-A (IASI, AMSU, MHS, AVHRR, HIRS, GOME, SBUV, ACAT)
  A-train (Aqua AIRS, AMSU, HSB, MODIS; Aura TES; CloudSat; and Calipso)
BAe-146-301
WB-57

## Slide 7
JAIVEx case April 27th, 2007:
over CART site, nighttime
(cloudy)
JAIVEx case April 29th, 2007
Over Gulf of Mexico, daytime
(~clear)
Background: IASI IR-imager; circles – IASI IFOVs; black line – NASA WB-57/NAST-I track
Two JAIVEx Cal/Val Flights Selected for Analysis:
CART site

## Slide 8
Horizontal cross-section of TAIR(P=850 mb), JAIVEx case Apr 27, 2007.
Five panels in each row correspond to 5 laps of NAST-I flight.
Retrievals are done for three instrument configuration.
“ABI+PHS” retrieval is much closer to the “Truth” than “ABI only”.

## Slide 9
Horizontal cross-section of relative humidity, P=500 mb, JAIVEx case Apr 27, 2007.
Five panels in each row correspond to 5 laps of NAST-I flight.
Retrievals are done for three instrument configuration.

## Slide 10
Horizontal cross-section for surface temperature, JAIVEx clear case Apr 29, 2007.

## Slide 11
ALOSE-1 validation experiment
  DOE ARM CART site, OK
  Dec 11-14, 2012
IASI, CrIS, AIRS overpasses (4-5 hours time difference) are accompanied with ground-based observations (ASSIST, AERI, sondes).
ABI radiances are simulated from all three hyperspectral instruments. IASI is chosen as referenced moment t0; then ABI/CrIS and ABI/AIRS are used as ABI observations at moments t1 and t2. After, ABI+PHS and ABI only retrievals are compared with retrievals from full resolution CrIS and AIRS.
ABI + PHS approach has a potential to improve the accuracy of ABI atmospheric soundings (but can not totally replace hyperspectral instruments!)

## Slide 12
Part II: Clouds: why are they so important?
Monthly Averaged Global Cloud Fraction 2005 – 2013:
Movie credit: http://www.earthobservatory.nasa.gov

## Slide 13
Main features:
Two training sets of atmospheric states and corresponding radiances: clear and cloudy
Cloudy sets are divided to 9 bins depending on PCLD in 1000-100 mb pressure range;
Retrieved products:
    T(p), H2O(p), O3(p)
    Surface characteristics: TSFC, eSFC(n)
    Cloud parameters: PCLD, HCLD, TCLD, e*(n) = effective cloud emissivity
Latest development:
Four methods for cloud bin classification:
    Residual fit of observed radiance with radiance EOFs;
    T-split
    CO2 – slicing
    Fit to referenced atmosphere (GDAS, ECMWF)
Effective cloud emissivity (product of cloud emissivity and cloud fraction)
Comprehensive quality control
All-sky Dual Regression Retrieval Algorithm
(in collaboration with University of Wisconsin – Madison)
Ultimate Goal: to make retrieval algorithm for clear and cloudy sky conditions.

## Slide 14
Dual Regression Algorithm Technique:
Step II: get “Cloud” retrieval
Step III: compare with sonde
Step I: get “Clear” retrieval

## Slide 15
Comparison with Dropsondes, JAIVEx case Apr. 27

## Slide 16
Retrieved Cloud Altitude, Apr. 27, 2007: Laps 1 to 5

## Slide 17
Retrieved Cloud Altitude, Apr. 29, 2007: Laps 1 to 7
MetOp AVHRR channel 1 (left, 0.58-0.68 mm) and channel 4 (right, 10.3-11.3 mm). Sunglint seriously contaminates the eastern part of the channel 1 image while SST variations and low level cloud influence the IR channel 4.

## Slide 18
NOAA Cal/Val data set for the “Focus Day” Oct 19, 2007 is used:
  236 granules of IASI radiances, 22-23 scans in each (total ~650,000 IFOVs)
  Corresponding ECMWF atmospheric states (T(p), 6 gases, surface)
The eff. cloud emissivity e*(n) = Cld_Frc * eCLD(n) is obtained with CO2 slicing method
Empirical model of the eff. cloud emissivity is created on this basis as a function of PCLD
Retrieval of the e*(n) PC-scores is incorporated into DR algorithm
The effective cloud emissivity retrieval:

## Slide 19
Effective cloud Emissivity e* (n): TRUE vs RETR (9 PCLD classes)
PCLD 1
PCLD 2
PCLD 3
PCLD 4
PCLD 5
PCLD 6
PCLD 7
PCLD 8
PCLD 9

## Slide 20
Summary:
Fast and accurate regression algorithm to retrieve atmospheric thermodynamic state, cloud and surface characteristics for GOES-R ABI is under development and intensive validation
The algorithm can process both, clear and cloudy, observation conditions and shows consistent retrievals of cloud parameters: cloud top altitude, pressure, and cloud fraction
GOES-R ABI has a potential for mesoscale atmospheric soundings in combination with JPSS observations, although can not fully replace having hyperspectral sounder on a geostationary satellite.