## Slide 1
Hyperspectral Remote Sensing of Tropical Coastal Environments: the use of HICO data to derive water quality parameters in SW Puerto Rico
Roy A. Armstrong, Ph.D.
NOAA-CREST, University of Puerto Rico, Mayagüez Campus
8th Annual NOAA‐CREST Symposium

## Slide 2: Introduction and Outline
Justification
Direct vs. Indirect Monitoring of Coral Reefs Using Remote Sensing
Sampling Sites and Measurements
  AOPs
  IOPs
  Water Quality Parameters
HICO Summary
Atmospheric Correction
Comparison with Field Rrs
Ongoing and Future Work

## Slide 3: Justification
Coral reefs are highly productive coastal ecosystems that are often described as the marine equivalent of terrestrial rainforests in terms of biodiversity.
Coral reefs are among the most threatened coastal ecosystems worldwide resulting in unprecedented degradation over the past few decades.
Recent accelerated coral reef decline is mostly related to anthropogenic impacts such as increased sedimentation and nutrient overloading.
There is an urgent need to monitor changes in water quality parameters that are detrimental to coral reefs.

## Slide 4: Direct vs. Indirect Monitoring of Coral Reefs Using Remote Sensing
Direct – includes benthic mapping and characterization of coral reefs and other biotopes using a “sensor down” approach.
For example, AVIRIS airborne hyperspectral data is combined with LiDAR bathymetry data to produce a benthic classification map of La Parguera. Requires atmospheric and water column corrections. See Poster #14.

## Slide 5: Direct vs. Indirect Monitoring of Coral Reefs Using Remote Sensing
Indirect – addresses the oceanic environment around the reef.
  Sea surface temperatures (SSTs) and bleaching events.
  Low salinities and high turbidity from episodic rainfall events.
  Water optical properties (AOP and IOP) and coral reef parameters.
MERIS 300 m derived Chl-a

## Slide 6: Water Optical Properties (AOP and IOP) and Coral Reef Parameters

## Slide 7: Sampling Sites

## Slide 8: Field Sampling: Instrumentation
Profiling sensor package that includes a CTD, a WetStar fluorometer, an ac-9 for absorption and attenuation, and a HydroScat-6 for backscattering.
GER-1500 spectroradiometer measures Lu, Ls, and Ed. This was used to calculate Rrs.
Surface water samples are used for measuring CDOM, Total Suspended Matter, and Chlorophyll.
Biogeochemical Properties
IOPs: a, c, bb
AOP: Lu, Ed, Rrs

## Slide 9: Water Quality Parameters
Median values for Chl-a, TSM, and CDOM absorption at 350 nm at the six stations.

## Slide 10: HICO Summary
HICO operating since September 25, 2009
Over 6000 scenes collected
Slot on ISS until July 2014
Data from OSU website – http://hico.coas.oregonstate.edu

## Slide 11: HICO Data

## Slide 12
Targets cover an area 50 km wide by 200 km long
One scene per orbit
Orbits
  NW to SE (descending)
  SW to NE (ascending)
87 bands (400 – 900 nm)
5.7 nm spectral resolution
SNR: 200:1
Total of 38 images to date
  15 are cloud free
  2 images with simultaneous field measurements
HICO Data for
Puerto Rico

## Slide 13: Atmospheric Correction
Slide courtesy of Z. Lee

## Slide 14: TAFKAA Vs. CSS Puerto Rico
Slide courtesy of Z. Lee

## Slide 15: TAFKAA Vs. CSS Puerto Rico
Slide courtesy of Z. Lee

## Slide 16: TAFKAA Vs. CSS Yangtze River
Slide courtesy of Z. Lee

## Slide 17
HICO September 20, 2012

## Slide 18: Variability of Field Rrs

## Slide 19: Comparison with Field Rrs
Field Rrs – G1
HICO Rrs – G1

## Slide 20: Comparison with Field Rrs

## Slide 21
Ongoing and future work
Quality control of field data
Spatial patterns and trends in AOPs, IOPs,
Chl-a, TSS, and CDOM
Algorithm development using derivative analysis
  Using field Rrs
  Using HICO data
Relate spatial patterns in water quality, as determined
by bio-optical properties to the condition of coral reefs

## Slide 22: Image-derived Kd values (Using AVIRIS Data)
Poster 14: Benthic Habitat Mapping for La PargueraMarine Reserve, Southwestern Puerto Rico, Using Passive and Active Remote Sensing Data.
William Hernandez, Doctoral Candidate, NOAA-CREST, UPRM-Mayaguez Campus

## Slide 23: Acknowledgments
Belitza Brocco and William Hernandez
Fernando Gilbes
Zhong Pin Lee
Curtiss Davis and the HICO Science Team
CariCOOS - IOOS – NOAA
NOAA CREST CSC