## Slide 1: An Agricultural Application of GOES-PRWEB
Dr. Eric Harmsen
Professor, Dept. of Agricultural and Biosystems Eng., Univ. of Puerto Rico-Mayaguez
Victor J. Reventos
Undergraduate Research Assistant, Dept. of Electric and Computer Eng., Univ. of Puerto Rico-Mayaguez
8th Annual NOAA CREST Symposium
The City College of City University of New York, NY
June 5-6, 2013

## Slide 2: GOES-PRWEB
25 daily hydro-climate variables published to internet
Solar Radiation Reference Evapotranspiration
Soil Moisture Actual Evapotranspiration
June 4th, 2013

## Slide 3: Objective
To show an agriculture application of GOES-PRWEB algorithm. Specifically:
  A simple web-based method for scheduling irrigation

## Slide 4: What is the problem?
There is anecdotal evidence that most farmers do not use scientific methods for scheduling irrigation
DEFINITION: Irrigation scheduling is the process used by irrigation system managers (farmers) to determine the correct frequency and duration of watering. (wikipedia.org)
Data from Idaho

## Slide 5: Why do we care?
Over application of water
Leads to the waste of
  water
  energy
  chemicals
  money
  may lead to the contamination of ground and surface waters.
  leaching of fertilizers past the root zone
  water logging
  lower crop yields.
Under-application of water
Lead to
  crop water stress
  reduced crop yields
  loss of revenue to the grower
“I wish I would have applied more irrigation.”

## Slide 6: How much water and money are we talking about?

## Slide 7: Global Agricultural Water Use
70% of all water withdrawn is used for agriculture and the majority of this water is used for irrigation.
Source of information: FAO

## Slide 8
Cotton
Pepper
Corn
Crop Yield vs. Water Applied/used
Wheat
Rice

## Slide 9: The Cost of Over-Applying Irrigation Water
Assume the following:
    Small 10-acre farm grows squash (calabaza)
    Four (4) month season
    Estimated consumptive use (CU) for season = 500 mm
    Actual potential CU for season = 400 mm
    Overall cost of water = $30/acre-ft (considering only: cost of water and electricity)
    Assume the normalized yield vs. CU curve in the next slide is applicable.
    Value of a typical squash crop (net income)* = $1,243/acre.
    *Conjunto Tecnológico para la producción de Calabaza, UPR Experment Station, Publication 155, revised 2012

## Slide 11: Example continued
Results:
    Excess water applied = 100 mm = 1.07 million gallons = 3 acre-ft (lost to groundwater)
    Normalized CU = 1.25, therefore normalized yield = 0.9 (or 0.1 loss)
    Potential $ LOST = cost of water + lost yield = 3 ac-ft x $30/ac-ft + [0.1*$1,243/ac] x 10 ac = $1,333
    $13,330 for 100 acres, 10.7 million gallons of water
    133,300 for 1000 acres, 107 million gallons of water
    FYI: Typical cost of irrigaiton water in U.S. is $200 per ac-ft
    If ag. chemicals are leached to groundwater , groundwater is potentially
    contaminated (cost was not included in calculation).

## Slide 12: Cost of Under-Applying Irrigation Water
Assume the following:
    Same squash farm (10-acres)
    Four (4) month season
    Estimated CU for season = 300 mm
    Actual potential CU for season = 400 mm
    Assume the normalized yield vs. CU curve is applicable.
    Value of a typical squash crop* = $1,243/acre.
    *Conjunto Tecnológico para la producción de Calabaza, UPR Experment Station, Publication 155, revised 2012

## Slide 13: Example continued
Results
  Water deficit = 100 mm
  With a normalized CU of 0.75, the normalized yield = 0.85 (or 0.15 loss)
  Potential $ LOST = lost yield = [0.15*$1,243/ac] x 10 ac = $1,864
  $18,640 for 100 acre
  180,640 for 1,000 acre
$1,864 could pay your daughter’s university tuition or pay her rent for 6 months
(tuition is cheap in PR)

## Slide 14: Surface Irrigation
Typical Irrigation Systems

## Slide 15: Sprinkler Irrigation

## Slide 16: Drip Irrigation

## Slide 17: Fertigation

## Slide 18: Drip Distribution Uniformity
Distribution Uniformity is critically important in Drip Irrigation
Why?
  Sometimes a plant only has one emitter. If the emitter is plugged, then the plant may die.
  If water is applied non-uniformly, then fertilizer will also be applied non-uniformly.

## Slide 19: How much water should we apply?
Evapotranspiration = evaporation from soil and wet surfaces + transpiration from leaves
Evapotranspiration = plant water requirement

## Slide 20: Determine Crop Water Requirement
ET = Kc ETo
where
ET = evapotranspiration = crop water requirement = consumptive use (CU)
Kc = Crop Coefficient (unique for every crop)
ETo = Reference Evapotranspiration (function of climate)

## Slide 21: Many weather stations ($1,700 approx.) will calculate the daily reference evapotranspiration

## Slide 22: What if a farmer doesn’t have a weather station? Here’s a simple web-based method for scheduling irrigation
Define problem (location, farm size, crop, etc.)
Determine ETo
Determine rainfall
from onsite gauge or NEXRAD
Estimate Crop Water Requirement
ETc = Kc ETo
Determine average Kc for the time period
Determine the number of hours to run the pump
T = 17.817 x [D x A]/[Q x eff]
Start
Harmsen E.W., 2012. TECHNICAL NOTE: A Simple Web-Based Method for Scheduling Irrigation in Puerto Rico J. Agric. Univ. P.R. 96 (3-4) 2012.

## Slide 23: Detailed Example
Determine the irrigation requirement for the 5 day period, February 15-19, 2012, for a tomato crop in Juana Diaz, Puerto Rico. Table 1 summarizes the information used in the example problem. Table 2 provides the important web addresses necessary for obtaining data for use in the example problem. Table 3 shows the crop growth stage and crop coefficient (Kc) data for the example problem.

## Slide 24
Table 1. Information used in example problem.
Table 2. Internet URLs for example problem.
Table 3. Crop growth stage and crop coefficient data for example problem.

## Slide 25: Rainfall
A rain gauge is not available on or near the farm; therefore, it is necessary to obtain rainfall information from NOAA’s MPE (NEXRAD and rain gauges in PR) radar. Inspection of the rainfall maps at the URL provided in Table 2 indicates that there was no rainfall during the five day period. Therefore, all of the crop water requirement will have to be satisfied with irrigation.

## Slide 26: Crop Coefficient
The averge Kc value of 0.85 for the five day period was obtained.
Crop coefficient curve for the example problem. The heavy dashed line applies to the example problem with day of season 46-50 (i.e., Feb 15-19) corresponding to an approximate crop coefficient of 0.85 (vertical axis).

## Slide 27: Reference Evapotranspiration (ETo) from GOES-PRWEB algorithm
The next step is to determine the reference evapotranspiration (ETo) for the five day period. The next slide shows the estimated reference evapotranspiration for Puerto Rico on February 15, 2012 obtained from the web address provided in Table 2.
The estimated ETo for the site location on 15 Feb., 2012 is 2.95 mm.
Using a similar procedure, the ETo values for Feb. 16, 17, 18 and 19 are 2.8 mm, 3.1 mm, 3.5 mm and 3.7 mm, respectively. Summing up the ETo values comes to a total reference evapotranspiration (for the five days) of 16.1 mm.

## Slide 28: Reference Evapotranspiration from GOES-PRWEB

## Slide 29: Crop Water Requirement
The crop water requirement (ET) for the time period can now be estimated as follows:
ETc = Kc ETo = (0.85)(16.1 mm) = 13. 7 mm

## Slide 30: Number of hours to run the pump to satisfy the crop water requirement
The final step is to determine the number of hours that the pump should be run to apply the 13.7 mm of water.
A form of the well-known irrigation equation (Fangmeier et al., 2005) can be used:
T = 17.817 x [D x A]/[Q x eff]
where T is time in hours, D is depth of irrigation water in mm, A is effective field area in acres, Q is flow rate in gallons per minute and eff is irrigation system efficiency.
Using D = 16.1 mm, A = 10 acres, Q = 300 gallons per minute and eff = 0.85, yields: T = 17.817 x [16.1 x 10] / [300 x 0.85]
= 11.25 hours.

## Slide 31: In Conclusion
Many farmers do not systematically schedule irrigation
Application of the wrong quantity of water can lead to losses in water, fuel, chemicals, yield and money.
A simple web-based method was introduced for scheduling irrigation on farms without weather stations.
The approach presented here is relatively simple and the near-real time data is available to any farmer in Puerto Rico with internet access.

## Slide 32: Future Work
Calibration of hydrologic components of GOES-PRWEB. Currently we are working on surface runoff, aquifer recharge and total stream flow.
Develop web tools to make the algorithm results easier for the public to use.
Adapt GOES-PRWEB to the island of Hispañola
Develop additional applications
  Potential crop yield
  Climate change evaluation